## Slide 1
Exercise 1: Hamming Code Analysis (12,8)
Problem: Analyze received code 0x0EA and identify original message
Given options: [0x5A, 0x3B, 0101101, 0xFA, 0xA2]
Steps:
1. Convert 0x0EA to binary:
0x0EA = 0000 1110 1010
2. Check parity bits
3. Extract message bits:
0101 1010 (0x5A)

## Slide 2
Exercise 2: Error Correction in Hamming Code
Problem: Analyze and correct received code 1011 1000 1110
Given options: [0xCC, 0xF4, 0xC9, 0xC6, 0xD5]
Steps:
1. Convert to hex: 0xB8E
2. Detect error at position 9
3. Correct the error:
1011 1000 1110 → 1011 1000 1010
4. Extract message: 1100 0110 (0xC6)

## Slide 3
Exercise 3: CRC Error Detection
Problem: Verify codeword 1100101 with G = 1001
Determine if codeword is correct, corrupted, or incomplete
Steps:
1. Polynomial Division:
Dividend: 1100101
Divisor: 1001 (G)
2. Check Remainder:
Remainder ≠ 0
3. Conclusion: Corrupted bits detected

## Slide 4
Exercise 4: Message Encoding with Generator Polynomial
Problem: Encode message M=0x9D using G=11001
Find the correctly received codeword
Steps:
1. Convert M to binary:
0x9D = 1001 1101
2. Append zeros (degree of G):
1001 1101 0000
3. Calculate remainder using polynomial division
4. Append remainder to original message

## Slide 5
Exercise 5: Cross Parity Encoding
Problem: Encode decimal digits 4-9 using Excess-3 code
Apply cross parity for error detection
Steps:
1. Excess-3 Encoding:
4 → 0111
5 → 1000
6 → 1001
7 → 1010
8 → 1011
9 → 1100

## Slide 6
Exercise 6: Cross Parity Verification
Problem: Verify sequence (010111101011111101000101)₂
Using even cross parity encoding
Steps:
1. Arrange bits in grid (6-bit blocks)
2. Check row parity
3. Check column parity
4. Identify any discrepancies

## Slide 7
Exercise 7: Linear Block Code Feasibility
Problem: Analyze feasibility of (20,16) linear block code
for single error correction
Steps:
1. Check feasibility criterion:
2^(n-k) ≥ n + 1
2. Calculate:
2^(20-16) = 2^4 = 16
n + 1 = 20 + 1 = 21
3. Compare: 16 < 21

## Slide 8
Exercise 8: Maximum Error Correction
Problem: Calculate maximum correctable errors
Given: n=63, k=57
Steps:
1. For single-error correction:
Minimum Hamming distance d = 3
2. Calculate max correctable errors:
t = ⌊(d-1)/2⌋ = 1

## Slide 9
Advanced Problem 1: Double-Error Detection
Problem: Determine minimum Hamming distance for:
- Double-bit error detection
- Single-error correction with double-error detection
Given: n=15, k=11, r=4
Steps:
1. For double-error detection:
dmin ≥ t + 1 = 3
2. For single correction + double detection:
dmin ≥ 2e + t + 1 = 5

## Slide 10
Advanced Problem 2: Syndrome Calculation
Problem: Calculate syndrome for Hamming(7,4) code
Received codeword: 1011101
Find and correct any errors
Steps:
1. Parity-Check Matrix H:
[1 1 1 0 1 0 0]
[1 0 0 1 1 0 1]
[0 1 0 1 0 1 1]
2. Calculate S = rHᵀ
3. Error position from syndrome: 5
4. Correct the error

## Slide 11
Advanced Problem 3: CRC Verification
Problem: Verify transmitted codeword using CRC
Message M = 1101, G(x) = x³ + x + 1
Transmitted: 11010111
Received: 11000111
Steps:
1. Convert G(x) to binary: 1011
2. Divide received code by G(x)
3. Check remainder
4. Locate and correct error

## Slide 12
Advanced Problem 4: Double-Error Correction Feasibility
Problem: Determine feasibility of double-error correction
Given: n=15, k=9
Steps:
1. Check criterion:
2^(n-k) ≥ 1 + n + n(n-1)/2
2. Calculate:
2^(15-9) = 2^6 = 64
1 + 15 + 15(14)/2 = 121
3. Compare: 64 < 121

## Slide 13
Advanced Problem 5: Maximum CRC Burst Error Detection
Problem: Find maximum detectable burst error length
Generator polynomial: G(x) = x⁴ + x³ + x + 1
Determine error detection capability
Steps:
1. Analyze generator polynomial:
G(x) = x⁴ + x³ + x + 1
Binary: 11011
2. Determine degree: r = 4
3. Maximum burst length = r

## Slide 14
Advanced Problem 6: EAN-13 Barcode Verification
Problem: Verify EAN-13 barcode 6291041500213
Calculate and verify check digit
Steps:
1. Weight digits alternately by 1 and 3:
6×1 + 2×3 + 9×1 + 1×3 + 0×1 + 4×3 +
1×1 + 5×3 + 0×1 + 0×3 + 2×1 + 1×3 = 82
2. Calculate check digit:
10 - (82 mod 10) = 8
3. Compare with given check digit (3)

## Slide 15
Advanced Problem 7: QR Code Error Correction
Problem: Analyze QR code with Level L (7%) recovery
Message: 'HELLO' with 2 damaged bytes
Determine recoverability
Steps:
1. Analyze error correction capacity:
Level L = 7% recovery
2. Assess damage:
2 bytes damaged
3. Check recoverability