## Slide 1
Slide 1: Exercise 1: Hamming Code Analysis (12,8)
Problem: Analyze received code 0x0EA and identify original message
Given options: [0x5A, 0x3B, 0101101, 0xFA, 0xA2]
Steps:
1. Convert 0x0EA to binary:
0x0EA = 0000 1110 1010
2. Check parity bits
3. Extract message bits:
0101 1010 (0x5A)

## Slide 2
Slide 2: Exercise 2: Error Correction in Hamming Code
Problem: Analyze and correct received code 1011 1000 1110
Given options: [0xCC, 0xF4, 0xC9, 0xC6, 0xD5]
Steps:
1. Convert to hex: 0xB8E
2. Detect error at position 9
3. Correct the error:
1011 1000 1110 → 1011 1000 1010
4. Extract message: 1100 0110 (0xC6)

## Slide 3
Slide 3: Advanced Problem 15: Maximum CRC Burst Error Detection
Problem: Find maximum detectable burst error length
Generator polynomial: G(x) = x⁴ + x³ + x + 1
Determine error detection capability
Steps:
1. Analyze generator polynomial:
G(x) = x⁴ + x³ + x + 1
Binary: 11011
2. Determine degree: r = 4
3. Maximum burst length = r